| Power Tool Usage and Personal Protective Equipment Requirements |  |
| --- | --- |
| Equipment type: Circular Saw | Date: |
| Department: | Employee: |
| Tool manufacturer: | Task: |
| Potential Hazard | Type of PPE Required | PPE Required (Yes / No) |
| Chips, Dust | Safety Glasses with side shields | Yes |
| Noise | Hearing Protection | Yes |
| Hot surfaces, rough surface materials | Heat and cut/puncture resistant gloves | Recommended |
| Precautions |  |
| Hot surface hazard. Do not touch the blade or cut surfaces immediately after use. | Use only correct blades in mounting. Use only blades with correct size holes. Do not use defective or incorrect washers or bolts |  |
| Keep guards in place and in working order. Do not use if lower guard does not close briskly over saw blade. Check for guard operation and straightness. |  |  |
| Keep blades clean and sharp. This will minimize stalling and kickback. If kickback occurs release switch immediately. |  |  |
| Guard against kickback. Kickback occurs when the saw stalls rapidly and is driven back toward the operator. Release switch immediately if machine stalls or saw binds. |  |  |