| Personal Protective Equipment Hazard Assessment Certification |  |
| --- | --- |
| Job Title: Maintenance Worker | Date: 10/16/00 |
| Department: Physical Plant, Housing, Power Plant | Supervisor: |
| Location / Worksite: | Analysis: Dan Beachnau |
| Employee Name(s): | Signature: |
| Tasks, Job Classification or Workstation | Potential Hazard | Type of PPE Required | PPE Required (Yes / No) |
| Arc Welding or Cutting | Electric shock, metal sparks, molten and hot metal, UV, IR and visible light, falling, dropping, rolling and sharp objects | Insulating mats or blankets, insulated/heat and puncture/cut resistant gloves, safety shoes, hard hat, safety glasses, welding shield or helmet with appropriate eye shade. | Y |
| Oxy-fuel Welding or Cutting | Metal sparks, molten and hot metal, UV, IR and visible light, falling, dropping, rolling and sharp objects | Heat and puncture/cut resistant gloves, safety shoes, hard hat, safety glasses, welding shield or helmet with appropriate eye shade. | Y |
| Torch Brazing | Metal sparks, molten and hot metal, UV, IR and visible light, falling, dropping, rolling and sharp objects | Heat and puncture/cut resistant gloves, safety shoes, hard hat, filer lens spectacles or goggles, or safety glasses and hand shield, with appropriate eye shade (at least #3). | Y |
| Torch Soldering | Molten and hot metal, UV, IR and visible light, falling, dropping, rolling and sharp objects | Heat and puncture/cut resistant gloves, flame resistant clothing, safety shoes, hard hat, filter lens spectacles or goggles, or safety glasses and hand shield, with appropriate eye shade (at least #2). | Y |
| Metal Grinding or Chipping | Metal sparks and chips, falling, dropping, rolling and sharp objects | Heat and puncture/cut resistant gloves, typical work clothing, safety shoes, safety glasses, full face shield. | Y |